## Slide 1
SYNOPSYS EDA
Process Architecture
8 core areas | RTL to GDSII | vs. Cadence / Siemens EDA
High
Medium
Low
DESIGN PIPELINE — RTL to GDSII
Sequential
1
Logic Synthesis
SDC Standard
RTL → gate-level netlist. SDC constraints (Synopsys-created IEEE standard). Technology mapping to foundry PDK. Fusion Compiler unifies with P&R.
2
Place & Route
IC Compiler II: floorplanning → placement → CTS → routing. Fusion Compiler merges with synthesis for physical-aware optimization.
3
Extraction + Timing Signoff
Foundry Req'd
StarRC parasitic extraction feeds PrimeTime. PrimeTime is foundry-mandated (TSMC, Samsung, Intel). The toll booth — no chip tapes out without it.
4
Physical Verification
IC Validator: DRC, LVS, ERC. Checks layout against foundry manufacturing rules. Competes with Siemens Calibre (historical leader).
VERIFICATION CONTINUUM
Parallel Track
5
RTL Simulation
60-70% Effort
VCS: gold-standard SystemVerilog/UVM simulator. 60-70% of chip design effort is verification. Massive testbench investments lock customers in.
6
Formal Verification
VC Formal: property checking, equivalence checking. SpyGlass: RTL lint, CDC, RDC analysis. Mathematical proof of correctness.
7
Debug & Analysis
Verdi: waveform debug across all verification engines. Deep integration with VCS creates unified debug experience. SpyGlass early checks.
8
Emulation & Prototyping
Hardware
ZeBu: hardware emulation ($5-30M systems). HAPS: FPGA prototyping for software bring-up. Multi-year depreciation cycles.
DESIGNWARE IP
USB • PCIe • DDR • Ethernet • HDMI • ARC Processors • RISC-V • Security IP • Foundation IP • Multi-generation lock-in • Royalty revenue
SENTAURUS TCAD + SILICON LIFECYCLE
Semiconductor process simulation • Device physics for foundries • Silicon.da analytics • In-chip monitoring • Design-to-silicon feedback • Upstream advantage

## Slide 2
CADENCE DESIGN SYSTEMS
Process Architecture
Chip to System | Analog-Centric Platform | vs. Synopsys / Siemens EDA
High
Medium
Low
DIGITAL IMPLEMENTATION
RTL to GDSII
1
Genus Synthesis
RTL → gate-level netlist. Competing with Synopsys Design Compiler. Gaining share. Tightly integrated with Innovus downstream.
2
Innovus Implementation
Place & route. Concurrent multi-objective optimization (timing, power, area, SI). Leading PPA at advanced nodes. Competes with ICC2.
3
Cerebrus AI Explorer
AI/ML
ML-driven autonomous design space exploration. Wraps Genus + Innovus + Tempus + Voltus. Requires full Cadence flow — creates pull-through.
VERIFICATION
4
Xcelium Simulation
SystemVerilog/UVM. Mixed-signal co-sim with Spectre is a key differentiator vs. Synopsys VCS.
5
JasperGold Formal
Leader
Leader in formal verification. Property checking, security, connectivity. Deep methodology lock-in.
HUB
Virtuoso + Spectre
Custom / Analog IC Design • ~75%+ Market Share • The Gravitational Center
Unassailable Moat
Virtuoso Layout Suite: decades of accumulated PCells, design rules. Every foundry delivers analog PDKs targeting Virtuoso first.
Spectre Simulation: foundry-qualified SPICE models validated against Spectre. ADE integration is seamless.
No credible alternative at scale. Synopsys Custom Compiler has minimal share. Switching = re-architecting everything.
Mixed-signal bridge: Xcelium + Spectre co-simulation is a key differentiator — transistor to full-chip in one flow.
SIGNOFF
6
Tempus Timing
Challenger
Static timing analysis. Gaining ground vs. Synopsys PrimeTime. Tighter Innovus integration. Foundries increasingly qualify both.
7
Voltus Power
IR drop, electromigration, dynamic power. Embedded in Innovus for in-design analysis. Standalone for signoff quality.
PCB & SYSTEM — Chip to Board (Synopsys has NO equivalent)
Unique to Cadence
8
Allegro PCB Designer
Dominant
High-end PCB layout. Dominates complex high-speed boards (networking, server, automotive). Deep constraint management. Library lock-in.
9
Sigrity SI/PI Analysis
Signal integrity, power integrity for PCBs and packages. Closed-loop with Allegro. Pre- and post-layout analysis.
10
Celsius Thermal
Electro-thermal simulation across IC, package, board. Full system thermal analysis. Newer product expanding the platform.
PALLADIUM EMULATION + PROTIUM
Hardware emulation ($5-30M systems) • FPGA prototyping • Multi-year depreciation lock-in • Co-leader with Synopsys ZeBu • Verification IP (VIP)
TENSILICA IP + DESIGN IP
Tensilica DSP/AI processors • Interface PHYs (DDR, PCIe, USB) • Memory compilers • Smaller IP portfolio than Synopsys DesignWare • Quantus extraction • Pegasus DRC/LVS